## Slide 1: Build-your-own Microcontroller Sensor Workshop

## Slide 2
Build-your-own Microcontroller Sensor Workshop
https://github.com/snguyen1/microcontroller-workshop-1

## Slide 3: What are we going to do?
Learn about microcontrollers
Learn about sensors
Little bit about electronics
Try to build temperature sensing circuit
Program a microcontroller

## Slide 4: About Microcontrollers
A small computer all in one chip
Has built-in:
  CPU
  Memory and Storage
  Some have WiFi or Bluetooth
Communicates by using input/output pins
Uses common communication protocols
Has various power needs
  Common is 5 volts or 3.3 volts

## Slide 5: About Sensors
Power needs
Digital VS. Analog
Protocols (I2C, SPI, “Serial”, others)
What is VCC, VDD, VIN, CLK and other labels you might find

## Slide 6: Power needs
Common Voltages
  5 volts
  3.3 volts
  1.5, 1.8, 2.5, 2.85 volts
  12 volts, -5.2 volts (ECL)
Logic Voltage
  TTL (Transistor to Transistor Logic)
    Uses 5 volts - i.e. 5v = on (1), and 0v = off (0)
  CMOS (Complementary metal–oxide–semiconductor)
    Uses supply voltage (i.e. 3.3 volts)

## Slide 7: Analog VS Digital
Analog
Variable values
Easy to translate
Can only send one value
Digital
On or Off (1 or 0)
Can send data easily
Could send multiple values (messages)

## Slide 8: Common Communication Protocols
I2C - Inter-Integrated Circuit
SPI - Serial Peripheral Interface
Serial - RS-232
TTL - Transistor to Transistor Logic
USB - Universal Serial Bus
CAN bus - Controlled Area Network
1-Wire
Wireless

## Slide 9: Common Communication Protocols
I2C - Inter-Integrated Circuit
Known as I-two-C, or I-Squared-C
Can send data pretty fast
Talks over two lines/wires
  SDA - Serial Data
  SCL - Serial Clock
Multiple devices can talk at the same over the same wires

## Slide 10: Common Communication Protocols
SPI - Serial Peripheral Interface
Can send data pretty fast
Multiple devices can talk over the same wires
Talks over four lines/wires
  MOSI - Master Out Slave In
  MISO - Mast In Slave Out
  SCK - Serial Clock
  SS1..SSn - Slave Select

## Slide 11: Common Pin Labels
VCC, VIN, V+, 5V, 3V3
  Supply voltage (usually 5 volts, or 3.3 volts.)
GND
  Ground or “negative” terminal
GPIO, D1..Dxx, A1..Axx
  General Purpose IO, Digital in/out, Analog in/out
SCK, SDA, MISO, MOSI, CS, SS
  Common communication protocol pins
CLK, ADC, DAC, HSPI, RTC, TOUCH

## Slide 12: Equipment
Notes: Let’s look at our parts.

## Slide 13: Breadboard
Half-size Breadboard
Easy to use
Quick prototyping
Reusable
No Soldering
Notes: Breadboard layout.

## Slide 14: Microcontroller Development Board
ESP32
Built-in Wireless
Many General Purpose I/O pins
Well established
Inexpensive
Readily Available
Notes: What is a microcontroller? It is a small computer that can communicate through pins on the board. Sometimes it’s a simple signal, like on or off. But it there are also more complex signals like serial data. There are several microcontrollers, we are are going to use this one.

## Slide 15: Environment Sensor
Bosch BME280
Low voltage (1.71V to 3.6V)
Temperature Range 0°C to 65°C
Measure Relative Humidity
Pressure from 300-1100 kPa
Accurate ±1°C
Low power consumption
Very small 2.5x2.5mm
Using I2C
Notes: But we are going to use this Bosch BME280 sensor. Which can measure temperature, humidity and pressure all at once, and as you can see it’s very small.

## Slide 16: Putting it together
Notes: We are going to do this in three steps, first we add the temperature sensor, then add the clock, then the sd card. And test each step so we know it works.

## Slide 17: Lesson 1
Notes: Next we need to program the microcontroller

## Slide 18
Microcontroller Pinout

## Slide 19
Microcontroller Pinout

## Slide 20
Add the Sensor

## Slide 21: Program the Microcontroller
Notes: Next we need to program the microcontroller

## Slide 22
Arduino IDE
Notes: Connect to microcontroller to the computer (USB). Start Arduino software. Select the (hopefully) correct port. Select the correct board (DOIT ESP-32)

## Slide 23: Lesson 2

## Slide 24: Real Time Clock
RTC DM3231
Flexible Power Requirements
Highly Accurate
Very Low Standby power consumption
Build-in very stable crystal oscillator.

## Slide 25
Add the RTC

## Slide 26: Lesson 3

## Slide 27: SD Card Reader/Writer
Micro SD Card Board
Accepts Micro SD cards
Common
Uses SPI

## Slide 28
Add the SD Card

## Slide 29: Wasn’t that fun?